## Slide 1
FlexiPath —
switch before the link fails
Keep a drone's control link, voice and video alive
when it moves between Wi-Fi, 5G, satellite and wired
networks. Switch before the signal fails.
TEAM TAROT CLUB
Al Ain University
EDGE GROUP CHALLENGE
Advanced Technology
Pioneers 2026
Fuad Ahamed
system architecture and software developer
Mohameden Sidi ahmed
networks and protocols research,
QoS/QoE guidelines
Reema Awad
experiments and data analysis
Nazer Alzaabi
product, demo and presentation
All members: Al Ain University
flexipath.vercel.app
LIVE PROTOTYPE
▶ TRY THE LIVE PROTOTYPE
flexipath.vercel.app
guided demo, simulator and the 2-minute video

## Slide 2
Executive summary
FlexiPath keeps critical connections alive with little extra power
PROBLEM
In our model, a legacy stack leaves one network before it joins the next. A moving
user loses the connection. When the control link (C2) of a drone is silent
for more than 300 ms, the drone must stop and hover (our piloted-flight rule).
MECHANISM
FlexiPath finds a fading signal seconds early. It wakes the next network and tests it. For 0.4 s, it sends only the critical commands on both networks. Then it switches with no gap. An anchor relay keeps each connection open.
Spare modems sleep at all other times to save power.
EVIDENCE
We run 160 paired simulated flights (8 scenarios, 5 seeds, 4 speeds) with a legacy stack and two existing methods. Reactive multipath (MPTCP/ATSSS) switches after failure. Always duplicate (PDCP duplication) sends twice.
With our 300 ms rule and 60 vs 250 ms outage detection, FlexiPath keeps C2 on 100 % of flights. A legacy stack keeps it on 0 %. Reactive multipath fails in three scenarios. Always duplicate uses 2.1–2.6× the power.
DELIVERED
4–7 points more reliability per extra watt for FlexiPath
versus 0.3–0.9 for always duplicate.
A working prototype (interactive 3D digital twin with a guided demo),
a deterministic simulation with a headless benchmark, and a documented model. We check its parameters against published data.
All results are from simulation; we claim no live-network measurements.

## Slide 3
The problem and why it matters
In our model, every network change costs a legacy stack 3.8 s of silence.
Dropped calls. Frozen streams.
300 ms of silence makes a drone hover.
Emergency response, industrial automation, connected transport and defence cannot wait.
Two drones, one route: Wi-Fi → 5G → satellite.
Stable baseline mission prep
Local coverage on the move
Wide-area coverage at speed
Global reach
beyond line of sight
CONTROL LINK (C2)
Command and control
PUSH-TO-TALK VOICE (REAL-TIME)
Clear, low-latency communications
CAMERA UPLOADS (BULK)
High-throughput data transfer
4. LEO SATELLITE
1. DOCK (WIRED)
2. WI-FI 6
3. 5G SA
Why drones: we model a hover after 300 ms without C2 (our piloted-flight rule).

## Slide 4
Existing mechanisms we analysed (criterion 01)
REACTIVE MULTIPATH
MPTCP backup subflow (RFC 8684) and 3GPP ATSSS active-standby.
Keeps a backup network on standby. It moves only after it confirms losses and the spare modem wakes up.
0.35 s
gap, more than our
300 ms C2 budget
1.20 W
low power
consumption
ALWAYS DUPLICATE
MPTCP redundant scheduler
and PDCP duplication.
Sends every important packet on two networks, all the time.
99–100 %
critical delivery
(most reliable)
2.65–3.39 W
high power consumption
and copies 49–100 % of protected bytes
Still fails when both paths fail together
(a shared radio shadow).
COMMON SHORTCOMINGS
Neither looks ahead.
Ignores the fading signal.
Ignores the known route.
Neither adds protection only at the moment a link fades.
WHAT WE ADAPT
Keep the anchored session (from multipath).
Keep the duplication (from PDCP), but use it only in a 400 ms burst around a predicted failure.
New in combination: prediction, route knowledge and traffic classes.
References: RFC 8684, Multipath TCP v1 (IETF, 2020) · 3GPP TS 23.501 §5.32, ATSSS · 3GPP TS 38.323, PDCP duplication · 3GPP TS 22.125 §7.2, UAV C2 KPIs · Related products: Elsight Halo, Peplink SpeedFusion, uAvionix muLTElink

## Slide 5
The FlexiPath mechanism
(criterion 02)
Continuous, zero-gap resilience
Measure the primary link ten times a second.
Spare modems sleep in DRX at
1.2 W and report signal once
per cycle.
Extend the signal trend to find where packet loss reaches 15 %.
Watch from 8 s to failure; act under 3 s.
The coverage map warns 8 s before a known shadow.
Wake the best spare modem (1.8 W) and test it with small 64-byte heartbeats.
Check its delay and loss before it carries anything.
For a 400 ms burst (3.4 W), send critical traffic on both paths. Add real-time traffic if its loss is over budget.
The receiver keeps the first copy of each sequence number and discards the late duplicate, so head-of-line delay is 0 ms.
Never copy bulk traffic; only pace it.
Make the tested network the main one with a 0 ms gap. Put the old radio back to sleep.
Connections stay open in a tunnel to the anchor relay.
A reversed trend cancels the prediction at no cost.
If an outage comes with no warning, use a fast failover (160 ms in our model).
01
02
05
04

## Slide 6
System design
One engine. Multiple radios. Continuous sessions.
APPLICATIONS
C2 link
(critical)
push-to-talk voice
(real-time)
camera and survey
uploads (bulk)
FLEXIPATH ENGINE ON VEHICLE
link monitor
and predictor
path scorer
traffic manager
replication, pacing, reordering buffer
radio power manager
DRX / warm probe /
burst
coverage map
EXPLAINABILITY AND DASHBOARD
current path
time-to-failure
alternate score
radio tier
action
DESIGNED TO SIT UNDER ANY COMMAND-AND-CONTROL APPLICATION
it needs no change to the application
ANCHOR RELAY
a fixed address
in the operator's network
the vehicle's
tunnel rebinds
across radios
the remote side
never changes
RADIOS
wired dock
port
link model:
signal, loss, RTT, jitter, capacity
Wi-Fi 6
link model:
signal, loss, RTT, jitter, capacity
link model:
signal, loss, RTT, jitter, capacity
LEO
satellite
link model:
signal, loss, RTT, jitter, capacity
it records each decision with the values at that tick:
reason
5G SA
trend

## Slide 7
Prototype, simulation and model (criterion 03)
flexipath.vercel.app
interactive 3D digital twin with mission and advanced views
guided demo
pauses at each real decision, explains what happened and which panel shows it
deterministic 10 Hz engine
seeded random streams with fading, capacity, loss, RTT, jitter, TCP and radio models
headless benchmark
scenarios A–H × 5 seeds × 4 speeds = 160 paired runs per stack, plus baselines and ablations; CSV output with 95 % CIs
published model
we check parameters against published measurements and test the 100 ms modem wake at 260 ms as a sensitivity run
Mission view of the live prototype. The FlexiPath drone (cyan) and the legacy-stack drone (crimson) fly with the same seed and radio conditions. The decision loop, decision card and scoreboard are around the twin.
▶ Try it yourself: flexipath.vercel.app · the guided demo, the simulator and the 2-minute video

## Slide 8
Results against the existing mechanisms (criterion 04)
Paired means over 20 runs per scenario, same seeds for every stack.
100%
of flights where FlexiPath keeps C2 (flight count) under our piloted
300 ms rule
1.2–4.6 s
FlexiPath acts before the path fails, versus 0.1–0.5 s after for reactive multipath
35%
fewer critical packets lost vs
reactive multipath (CI 30–39 %);
held-out; ~20 % with equal detection
4.0-7.1 pp/W
Reliability per extra watt versus
reactive multipath
(16.9–24.5 in D)
4.5-21×
FlexiPath's extra watts give 4.5–21× more reliability than always duplicate's
0.3–0.9 pp/W
Reliability against radio power, scenarios A–D, G and H (paired means). FlexiPath is between the two existing designs. It gives 0.6–1.2 points more critical delivery than reactive multipath for 0.05–0.18 W more. It uses 2.1–2.6× less power than always duplicate.
Flights that keep C2 under the piloted 300 ms rule (Legacy · Reactive multipath · Always duplicate · FlexiPath): A, B, C 0 · 100 · 100 · 100 — D 0 · 0 · 100 · 100 — G, shared radio shadow 0 · 0 · 40 · 100 — H, map out of date 0 · 0 · 100 · 100.
Robustness: the ablations show trend prediction gives the gain; in our model, the burst adds no measurable reliability. The results hold on held-out seeds. Under the 1 s waypoint rule, every multipath stack keeps C2. So the piloted-rule advantage needs a spare modem that resumes fast.

## Slide 9
Guidelines for QoS and QoE
across heterogeneous networks (criterion 05)
01
Anchor the session, not the interface — a fixed anchor relay prevents every reset.
02
Act on the trend, not on the failure — a 3 s signal trend gives seconds of warning.
03
Prepare the next path just in time, and only then — test it at 1.8 W; do not keep radios on.
04
05
06
Detect a failed path faster than the application allows — within the 300 ms C2 budget.
07
Measure what users feel, on matched pairs: interruption, delivery, voice MOS, power, same seeds.
09
Use what you know about the route — a coverage map is better than reaction if two radios fail together.
Duplicate only what needs it, only around the handover — a 400 ms burst costs ≈ 1 % of protected bytes.
Hold still unless a move clearly helps — a reversed trend cancels the prediction at no cost.
Deliver the first copy; never make real-time traffic wait in order.
08

## Slide 10
Plan for real-life use, limits, and declaration
Deployment path, known limits, and our AI-use declaration
DEPLOYMENT
A userspace agent on the vehicle's companion computer (Linux) controls modems through standard interfaces.
The anchor relay is at the operator's ground station or cloud edge.
It runs under current C2 and video applications; they need no change.
LIMITS
All results are simulated.
We evaluate the radio model at ground level.
Piloted rule needs a spare modem that resumes in ~100 ms
(5G RRC_INACTIVE or connected-mode DRX).
At 260 ms, an unexpected outage still forces a hover.
REAL-LIFE USE
Phase 1 (bench): laptop with Wi-Fi and a 5G dongle runs the included handover probe to measure one real network change. Phase 2 (field): test drone with Wi-Fi, 5G and a LEO terminal on a surveyed corridor; first survey flights build the coverage map. Phase 3 (pilot): one operator, one corridor, the paired-comparison method of this study applied to real flights.
AI-USE DECLARATION
AI tools (Anthropic Claude) helped with code, analysis drafts,
this deck and the video. An AI voice (Kokoro) reads the narration.
The design decisions, the experiments and their interpretation are
the team’s own, and every member can explain their part in their own words.
▶ TRY THE LIVE PROTOTYPE
flexipath.vercel.app
guided demo, simulator and the 2-minute video